## Slide 1: FPS technical meeting 14th November 2019
Dr Andrew Bond

## Slide 2: Eurocode 7 Parts 2 and 3 – Final PT Drafts October 2019 Timetable for submitting UK comments
End October 2019 – Final PT drafts of Eurocode 7 Parts 2 and 3 issued
5th-6th December 2019 – SC7 Working Groups meeting in Delft (to discuss)
Comments on these drafts to come through NSBs (i.e. BSI)
11th-18th January 2020 – B/526/3 Task Groups to prepare preliminary comments
20th January – B/526/3 meeting at Arups
(27th January – backup for overflow meeting)
End January 2020 – Deadline for submission of comments by NSBs
End April 2020 – deadline for Final PT versions of Eurocode 7 Parts 2 and 3
Documents still have to go to Formal Vote

## Slide 3: PT4 Final Draft October 2019 Classification of piles

## Slide 4: PT4 Final Draft October 2019 Examples of pile types in different classes

## Slide 5: PT4 Final Draft October 2019 Classification of information used to validate pile design

## Slide 6: PT4 Final Draft October 2019 Partial factors for pile resistance

## Slide 7: PT4 Final Draft October 2019 Pile design by calculation Method A ‘Ground Model Method’
Option | G | Q | Independent validation | Rd | FoS | Pile type | t | b | s*
(c) DC1 | 1.35 | 1.5 |  |  | ? |  |  | - | -
(d) DC3 | 1.0 | 1.3 | Minimum | 1.8 | 2.7-3.3 | Bored CFA Low displacement High displacement | 1.5 1.4 1.35 1.3 | 1.6 1.45 1.35 1.3 | 1.3 1.3 1.3 1.3
 |  |  | Limited | 1.55 | 2.3-2.9 |  |  |  | 
 |  |  | Comprehensive | 1.3 | 1.9-2.4 |  |  |  | 

## Slide 8: Pile design by calculation Method A ‘Ground Model Method’ Alternative based on DC1
Option | G | Q | Independent validation | Rd | FoS | Pile type | Rc | Rb | Rs
(c) DC1 | 1.35 | 1.5 |  |  | ? |  |  | - | -
(d) DC1 | 1.35 | 1.5 | Minimum | 1.6 | 2.5-3.2 | Bored CFA Low displacement High displacement | 1.4 1.4 1.3 1.2 | 1.4 1.4 1.3 1.2 | 1.2 1.2 1.1 1.1
 |  |  | Limited | 1.4 | 2.2-2.8 |  |  |  | 
 |  |  | Comprehensive | 1.2 | 1.9-2.4 |  |  |  | 

## Slide 9: Traditional factors-of-safety vs Eurocode 7 UK NA Bond and Harris (2008) †

## Slide 10: Global FoS with amended new proposal (50% G + 50% Q) (left) Base and shaft factors (right) Total factor

## Slide 11: PT4 Final Draft October 2019 Minimum validation testing/minimum pile spacing

## Slide 12: PT4 Final Draft October 2019 Test proof load
Proof load for Investigation Tests:
When Rrep is unknown at the time of test:
Proof load for Control Tests:

## Slide 13: PT4 Final Draft October 2019 Combination of actions for downdrag – guidance requested!
Downdrag treated as leading variable action:
More rigorous presentation (based on EN 1990):

## Slide 14: Existing UK pile design practice

## Slide 15: Traditional factors-of-safety vs Eurocode 7 UK NA Bond and Harris (2008) †

## Slide 16: Pile design by calculation Method A ‘Ground Model Method’ Alternative based on DC1 – CFA/Bored piles only
Option | G | Q | Independent validation | Rd | FoS | Pile type | Rc | Rb | Rs
(c) DC1 | 1.35 | 1.5 |  |  | ? |  |  | - | -
(d) DC1 | 1.35 | 1.5 | Minimum | 1.6 | 2.6-3.2 | Bored/CFA | 1.4 | 1.4 | 1.2
 |  |  | Limited | 1.4 | 2.3-2.8 |  |  |  | 
 |  |  | Comprehensive | 1.2 | 2.0-2.4 |  |  |  |